# Direction for use

# :

View time setting：

- After plugging AC110V, the preset timing 12:00 will be displayed on the screen

- . Press down to display on the screen the pump’s and the solenoid valve‘s start-up time: 0-60 minutes; 1- 60 second (default 1 second).

- Second: Set press release to display on the screen the time to shut down the spray:  0 – 60 minutes; 1- 60 seconds (default 1 second)

- Third: Press down to display the pressure release time 1-10 seconds (default 1 second).

- Fourth: Press down to return back to the original displayed time on the screen, which is 12:00

Press On to start the spray timing

Press Off to shut down the spray timing. Ps:

Ps: the spray and the pressure release time is complete they will shut down at once. ( at this period there will be no water pressure in the tube). (1)If you shut down and restart: (1). ( the computer’s clock has to be reset again). But the spray and the pressure release timing and 和三組 setting time have been recorded. (2). Shutting down and restarting, the computer will maintain a stable situation. Example : when there is no power it is “ On” ; after the power comes back the computer will automatically start.

Setting- spraying intervals and pressure release and the 3 sets settings.

- Set direct pressure for 3 seconds, enter setting mode, set release.

- When starting the spray, there will be a sparkle, Set the spraying time, 0-60 minutes 1-60 seconds, press ON, to increase the number of minutes, press Off to increase the number of seconds. Pressing directly for 2 seconds on On or Off, automatically increase or decrease the minutes or seconds.

- Second : Press set to, “ shut down spray”,will sparkle, set shut up period 0-60 minutes 1-60 seconds, press ON, to increase the number of minutes, press Off to increase the number of seconds. Pressing directly for 2 seconds on On or Off, automatically increase or decrease the minutes or seconds.

- Third: Press set and “ pressure release time” will sparkle, set pressure release timing: 1-10 seconds, press OFF to increase the seconds. Pressing Off for 2 seconds automatically increases the seconds.

- Fourth : Press on “ set time 1 ON”  sparkle, 1 start timing, press down ON to increase the timing, OFF to increase the minutes. Pressing directly ON, or OFF for 2 seconds will automatically increase the when or the minutes.

- Fifth: Press on , “ set time 1 OFF” to sparkle, set timing 1 shut down. Press ON to increase the timing, OFF to increase the minutes. Pressing directly ON, or OFF for 2 seconds will automatically increase the when or the minutes.

- Sixth: Press on , “ set time 2 ON”, when setting time start sparkling;  2 start up timing. Press ON to increase the timing, OFF to increase the minutes. Pressing directly ON, or OFF for 2 seconds will automatically increase the minut. when or the minutes.

- Seventh: Press on “ set time 2 OFF” when setting time start sparkling; 2 start up timing. Press ON to increase the timing, OFF to increase the minutes. Pressing directly ON, or OFF for 2 seconds will automatically increase the when or the minutes.

- Eighth: Press on “ set time 3 ON” when setting time start sparkling; 3 start up timing. Press ON to increase the timing, OFF to increase the minutes. Pressing directly ON, or OFF for 2 seconds will automatically increase the minut when or the minutes.

- Press on “ set time 3 OFF” when setting time start sparkling; 3 start up timing. Press ON to increase the timing, OFF to increase the minutes. Pressing directly ON, or OFF for 2 seconds will automatically increase the number of min when or the minutes.

- Tenth: Press down set, when timing display start sparkling (set clock time), Press ON to increase the number of hours, directly pressing On or OFF for 2 seconds will automatically increase the number of minutes when or minutes.

- Eleventh Setting: Press to return back to return back to timing

Setting up the three sets: Starting and Shutting down

(1)  Set and ON at the same time and press to start time setting ( 1 timing period)

(1)  Set and ON at the same time and press to set shutting down timing (1 timing period)

(2)  Set and OFF at the same time and press on timing to set starting up time ( 2 timing period)

(2)  Set and OFF at the same time and press on timing to set shutting down timing ( 2 timing period)

(3)  Press ON and OFF at the same time, starting period is about 3 hours

(3)   Press ON and OFF at the same time, shut down period is about 3 hours

black power cord : 110V~220V

Cable

1.Connect the red color to pump

2.Connect yellow to the water inlet solenoid valve

3.Connect the black to the high pressure solenoid valve

4.Connect the black cable to low Pressure solenoid valve.